## Slide 1: Stromerzeugungs- modellierung

## Slide 2: Allgemeines Vorgehen: PV & Windmodellierung
MaStR
ERA5
Profile Kapazitätsfaktoren
Aggregation
~500 Messpunkte in DE
Deutsches Register für Kraftwerke mit detailierten
Kraftwerksdaten
Monatlich modellierte Stromerzeugung Anlage
Jährlich modellierte Stromerzeugung Anlage
CO2 Einsparungspotential Anlage

## Slide 3: Modellierung Windstromerzeugung
Windkraftanlage VESTAS TYP: V90/2000
Nennleistung: 2000 kW
Durchmesser: 90 m
Min. Nabenhöhe: 80 m
Max. Nabenhöhe: 125 m
Windgeschwindigkeit auf Nabenhöhe
Die Leistungskurve und Windgeschwindigkeit auf Nabenhöhe
sind für Windmodellierung die relevante Größe
Bsp. 1 Typ
Leistungskurven von Turbinentypen
unterscheiden sich

## Slide 4: Modellierung Windstromerzeugung
ERA 5
wind speed @ 100m,10m
temperature @ 2m
pressure @ 2m
roughness length
Wind speed correction
Temperature correction
Pressure correction
Wind speed normalization
Input data per weather cell
Air density calculation
Turbine
DB
MaStR

## Slide 5: Modellierung Solarstromerzeugung
Solare Einstrahlung,
Temperatur
Zelle,
Modulspezifika,
= ( , , )
IGH | Global horizontal irradiation
IDH | Direct horizontal irradiation
ALB | Albedo
P | Pressure
T | Temperature
W | Wind speed
loc [latitude, longitude, altitude] | Location
time [year, month, day, hour] | Time
surf [tilt, azimuth] | Surface orientation
par | Module parameter
ERA5
MaStR

## Slide 6: Modellierung Bestrahlung auf einer geneigten Fläche
ERA 5 Data
IGH | Global horizontal irradiation
IDH | Direct horizontal irradiation
ALB | Albedo
P | Pressure
T | Temperature
W | Wind speed
Location/Time
loc [latitude, longitude, altitude] | Location
time [year, month, day, hour] | Time
 Diffuse Horizontal Irradiation
Technology Specification
surf [tilt, azimuth] | Surface orientation
par | Module parameter
MaStR
MaStR
ERA5
pvl_spa (Reda and Andreas 2004)
pvl_singleaxis (Lorenzo, E et al., 2011)
aoi_projection (King et al. 1997)
- Sky Diffuse
- Ground Diffuse
Direct Normal Irradiation
Diffuse Irradiation
Total Irradiation
PV module performance (based on PVLIB)
F1 = max(0,polyval(, AM)); #Spectral loss function
F2 = max(0,polyval(, )); #Angle of incidence loss function
)*SF; #Effective irradiance
effective irradiation cells | sapm_effective_irradiance
= (, , W, T, ) pvl_sapm_cell
cell temperature (King, D. et al, 2004)
= ( , , ) pvl_sapm
performance (King, D. et al, 2004)

## Slide 7: Ergebnisse Solar
Keine großen Standort Unterschiede
Wetterjahre zwischen 2000 – 2023 haben monatlich keine großen Ausreißer, unterscheiden sich aber

## Slide 8: Ergebnisse Solar
Standort

## Slide 9: Ergebnisse Wind
120m VS 100m
Standort
Standort & Nabehhöhe
Notes: niedersachsen
schleswig holstein
ausbau norden VS ausbau freiburg

## Slide 10: Modellierung Bestrahlung auf einer geneigten Fläche
ERA 5 Data
IGH | Global horizontal irradiation
IDH | Direct horizontal irradiation
ALB | Albedo
P | Pressure
T | Temperature
W | Wind speed
Location/Time
loc [latitude, longitude, altitude] | Location
time [year, month, day, hour] | Time
 Diffuse Horizontal Irradiation
Technology Specification
surf [tilt, azimuth] | Surface orientation
par | Module parameter
MaStR
MaStR
ERA5
pvl_spa (Reda and Andreas 2004)
pvl_singleaxis (Lorenzo, E et al., 2011)
pvl_get_aoi (King et al. 1997)
- Sky Diffuse
- Ground Diffuse
Direct Normal Irradiation
Diffuse Irradiation
Total Irradiation
PV module performance (based on PVLIB)
F1 = max(0,polyval(, AM)); #Spectral loss function
F2 = max(0,polyval(, )); #Angle of incidence loss function
)*SF; #Effective irradiance
effective irradiation in the cells
= (, , W, T, ) pvl_sapmcelltemp
cell temperature (King, D. et al, 2004)
= ( , , ) pvl_sapm
performance (King, D. et al, 2004)
https://pvlib-python.readthedocs.io/en/stable/reference/generated/pvlib.solarposition.spa_python.html?highlight=spa
https://pvlib-python.readthedocs.io/en/stable/reference/generated/pvlib.pvsystem.Array.get_aoi.html?highlight=Angle%20of%20incidence
https://pvlib-python.readthedocs.io/en/stable/_modules/pvlib/irradiance.html?highlight=Direct%20Normal%20Irradiation